ELECTRICAL CALCULATIONS FOR LIGHTING

- Most household electrical outlets are 110 or 120 Volts.

- Most homes constructed in the last 30 years have circuit breakers supplying each outlet with either 15 amps or 20 amps (it is usually written on the breaker).

- Most buildings constructed in the last 30-40 years have circuit breakers supplying each branch of outlets with 20 Amps.

Watts divided by Volts = Amps

Three lamps are plugged in and each has the following wattage: 1) 1,000W; 2) 1,000W; 3) 500W

The total wattage is 2,500 Watts

Electrical outlets are usually 110 or 120 Volts.  Round this number off to 100.

2500W / 100 V = 25 Amps (A 20 Amp breaker would be blown if the wattage of the lamps exceeded 2500)

Note:  Most video equipment such as external monitors and tape decks, as well as the cameras themselves, operate on about 15 – 20 watts.