CSD- UNIT 2 – Wheel and Tire Diagnosis and Repair

CTAE Resource Network

Wheel Rims- The assembly on which the tire is mounted

Wheel Bearings- Ball or roller bearing assemblies that reduce friction and support the wheels and axles as they rotate.

Lug Bolts-  Large steel nuts used to hold a wheel to the axle hub.

Lug Nuts- Threaded bolts or studs that are press-fit into an axle, hub, or brake rotor and accept lug nuts to mount wheels.

Tapered Roller Bearings- A bearing that utilizes a series of tapered steel rollers that operate between an outer and inner race.

Straight Roller- A bearing which uses straight, non-tapered rollers in its construction.

Ball Bearings- A bearing consisting an inner and outer hardened steel race separated by a series of hardened steel balls.

Tire Rating- A series of numbers and letter that designate how a particular tire will perform under different conditions.

Tire Valve- The means of adding air to the tire and wheel assembly.

Static Balance- Condition where a tire’s weight mass is evenly distributed around the axis of rotation. If the wheel is raised from the floor and spun several times, it should always stop in a different place.

Dynamic Balance- Condition when the weight mass is in the same plane as the centerline of the wheel.