CSD- UNIT 5 - Steering Systems, Diagnosis and Repair

CTAE Resource Network

Steering Arms- An arm bolted or forged to the steering knuckle. Used to transmit force from the tie rod to the knuckle.

Parallelogram Linkage- A steering system utilizing two short tie rods connected to steering arms and to a long center link. The link is supported on one en of an idler arm and the other end is attached to a pitman arm. The arrangement forms a parallelogram shape.

Rack-and-pinion Linkage- Steering system that contains fewer linkage components than the parallelogram system. There is no pitman arm, idler arm, or center link. The steering column shaft is connected directly to the pinion or sector shaft. The pinion operates the rack section, which operates the tie rods and, therefore, the steering knuckles.

Steering Shaft- A two piece shaft that transfers turning motion from the steering wheel to the gearbox.

Steering Gear- The assembly containing the gears, valves and other components used to multiply turning force.

Power Steering Pump- A belt-driven pump that provides hydraulic pressure to assist in the driver’s turning efforts.

Electronic Steering Control System- Electronic steering control that reduces power steering assist at cruising speeds to increase control and road feel. And increase assist at low speeds to facilitate parking.