PATHWAY:      Transportation Logistical Operations and Support

COURSE:  	Electrical/Electronic Systems Design

UNIT 5: 	System Testing and Charging System Service

Introduction

Annotation:

Shop safety issues are to be reviewed and stressed in this lesson. Students will identify the importance of safe tool use. Students will review basic electrical principles. Emphasis will be placed on the importance of correct electrical testing procedures in the lab exercise. Also included is a review of the use of (DMM) multimeter, electrical test equipment, and circuit wiring diagrams. Students will use factory service information to service electrical systems.

Grade(s):

| x | 9th |
| --- | --- |
| x | 10th |
| x | 11th |
| x | 12th |

Time:

6 (2 hour periods)

Author:

Sonny Reeves  sreeves.hutchingscc@bibb.k12.ga.us  www.autoteacher.net

Additional Author(s):

Students with Disabilities:

For students with disabilities, the instructor should refer to the student's IEP to be sure that the accommodations specified are being provided. Instructors should also familiarize themselves with the provisions of Behavior Intervention Plans that may be part of a student's IEP. Frequent consultation with a student's special education instructor will be beneficial in providing appropriate differentiation.

Focus Standards

GPS Focus Standards:

ACT-ESD-4: Demonstrate knowledge of charging system concepts, diagnosis, and repair.

GPS Academic Standards:

SPS9, Students will investigate the properties of waves.

ELA11W3, The student uses research and technology to support writing.

National Academic Standards (NATEF):

LA020, The technician uses study habits and methods when consulting the manufacturer’s publications, e.g., shop manuals, references, and computer databases.

MA187, The technician can use formulas to indirectly measure systems that are outside of the manufacturer’s specifications.

SC214, The technician can explain the relationship between electrical current in a conductor and magnetic field when produced in a coil such as the starter solenoid.

NATEF Standards:

VI.  ELECTRICAL/ELECTRONIC SYSTEMS

D.  Charging System Diagnosis and Repair

1. Perform charging system output test; determine necessary action.

2. Diagnose charging system for the cause of undercharge, no-charge, and overcharge conditions.

3. Inspect, adjust, or replace generator (alternator) drive belts, pulleys, and tensioners; check pulley and belt alignment.

4. Remove, inspect, and install generator (alternator).

5. Perform charging circuit voltage drop tests; determine necessary action

Understandings & Goals

Enduring Understandings:

Students will understand that the physics of electrical principles will continue regardless of advances in vehicle charging system technology.

Essential Questions:

What are the safety concerns for the technician servicing charging systems?

What chemicals are used in alternator service?

What hand tools are special to charging system service?

Why should the technician use protective clothing and equipment?

Why are clean, orderly work habits important?

What are the health and safety regulations for working with electrical systems?

Why are accurate measurements important to the electrical technician?

What specialized test equipment is used in charging system service?

What do “I” need to know about the automotive charging system in order to diagnose and repair charging system related concerns?

Knowledge from this Unit:

Students will learn what a charging system does.

Students will learn how to service a charging system.

Skills from this Unit:

Students will know the different parts in a charging system.

Student will know how to properly service a charging system.

Assessment(s)

Assessment Method Type: Select one or more of the following. Please consider the type(s) of differentiated instruction you will be using in the classroom.

|  | Pre-test |
| --- | --- |
|  | Objective assessment - multiple-choice, true- false, etc. |
|  | __ Quizzes/Tests __ Unit test |
|  | Group project |
|  | Individual project |
| x | Self-assessment - May include practice quizzes, games, simulations, checklists, etc. |
|  | _x_ Self-check rubrics __ Self-check during writing/planning process __ Journal reflections on concepts, personal experiences and impact on one’s life __ Reflect on evaluations of work from teachers, business partners, and competition judges __ Academic prompts _x_ Practice quizzes/tests |
|  | Subjective assessment/Informal observations |
|  | __ Essay tests __ Observe students working with partners __ Observe students role playing |
| x | Peer-assessment |
|  | __ Peer editing & commentary of products/projects/presentations using rubrics _x_ Peer editing and/or critiquing |
|  | Dialogue and Discussion |
|  | __ Student/teacher conferences __ Partner and small group discussions __ Whole group discussions __ Interaction with/feedback from community members/speakers and business partners |
|  | Constructed Responses |
|  | __ Chart good reading/writing/listening/speaking habits __ Application of skills to real-life situations/scenarios |
|  | Post-test |

Assessment(s) Title:

Checking a Charging system

Assessment(s) Description/Directions:

Use the handout download free from site to assess student learning or to allow peer review during practice sessions.

Assess student performance using;     Rubric titled “Charging” from this site

https://www.autoteacher.net/Electrical_Performance_TC1I.html

Attachments for Assessment(s):

How to use the performance task test. When students complete job sheet, and/or follow activity guide and have practiced the tasks the instructor may use the attached performance test for final assessment and to prove their level of mastery for unit. The performance test may be used by students during practice for peer assessment before instructor sign off. The completed rubric is placed in student portfolio for future reference. The performance test may be modified to suit individual teacher/student needs.

Learning Experiences

Instructional planning: Include lessons, activities and other learning experiences in this section with a brief description of the activities to ensure student acquisition of the knowledge and skills addressed in the standards. Complete the sequence of instruction for each lesson/task in the unit.

Sequence of Instruction

1.  Identify the Standards. Standards should be posted in the classroom for each lesson.

2.  Review Essential Questions.

3.  Identify and review the unit vocabulary.

4.  Assessment Activity.

Step 1

Introduce students to the charging system with review and research of alternator operation. Review electrical principles with emphasis on current flow. Explain inductive pick-up operation. Begin testing with review of safety in the use of electrical testing. Warn students of the dangers associated with typical lead-acid batteries. Remind students to never open circuit a live charging system on a late model vehicle as possible computer damage may occur. Refer to previous lesson on shop safety. Use a live 12-volt automotive battery or vehicle system for this demonstration. Demonstrate what occurs when a direct short is put into a circuit in a controlled, safe manner. Measure current flow with an inductive probe during demonstration. Use a covered or remote battery for students to experience safety precautions. You may want to use a set of dry cell 6-volt batteries to prevent explosions of hydrogen gas. Be sure to stress the dangers of working on live circuits, wet cell batteries, and electrical components. Insure students remove any metal jewelry before working with electrical circuits.

Web resource for step 1

Title: Charging system principles

URL: www.autoshop101.com

Annotation:  Free resource for information on theory and operation of charging systems

Step 2

Review electrical principles. Stress the three measurements of voltage, ohms and amperage. Describe how an inductive lead works. Have students access electrical course on Gordon Worobec’s Web site or show on interactive white board with projector. Show theory and operation of starting and charging circuit electrical circuits. Discuss operation and design. Have students research Fluke Web site for information on digital multimeters and current flow testing. Demonstrate meter use to students. Have examples of electrical components to pass around in the class to emphasize key points of electrical principles.

Web Resources for Step 2

Title: Mr. Worobec's Electrical Course
URL: http://gworobec.users.50megs.com/site1010.html
Annotation: Online electrical course covers theory and operation of basic automotive charging and starting systems.

Title: Fluke Electrical Testing Site
URL: http://www.fluke.com/application_notes/automotive/circuit.asp?AGID=1&SID=103#volt
Annotation: Fluke's automotive test site demonstrates the use of multimeters to test automotive starting and charging systems.

Title: Electrical Electronics Training
URL:   http://www.electude.com/

Annotation: Interactive web site with electrical/electronics training and testing procedures in several formats Very good explanation of wiring diagrams, relays and electrical principles. This elearning site Involves active and critical thinking of the learner in a virtual reality 3d animation online.

Step 3

Demonstrate use of starting/charging system tester. Empathize key safety precautions when using the test equipment. Demonstrate use of multimeter to measure electrical levels. Use an example of a charging circuit to show how resistance and continuity relate in testing. Stress importance of proper procedure in testing circuits for volts and amperage. Do not allow students to damage meters! Make sure they are fused. Add fuse to lead if needed. If you are using a wet cell battery consider placing it in a protective box or remote location to prevent explosion. Demonstrate use of voltmeter in low and high voltage mode. Demonstrate use of amp probe and low/high amp testing. Allow students to practice use of meter and measurement tools. Reinforce math skills from earlier lessons.

Web Resources for Step 3

Title: Fluke Meter Use Site
URL: http://www.fluke.com/application_notes/automotive/beatbook.asp?AGID=1&SID=103
Annotation: Training site for use of multimeters.

Step 4

Demonstrate the use of inductive test on live vehicle that is in good condition. Show students examples of meter use to test current throughout circuit. Demonstrate resistance in a circuit. Prepare a “problem” circuit on the vehicle and demonstrate finding the volt drop with the meter. Demonstrate measuring, starting, and charging amperage levels. Loosen the alternator belt to show what happens with loose drive belt. Give students examples of worn belts. Demonstrate how tensioners operate on serpentine belt vehicles. Show how to test for loose belt and judge proper tension. Discuss service problems and solutions of the different belt problems technicians may encounter. Allow students to research engine drive belts on Internet.

Step:  5

Demonstrate use of low amp probe on live vehicle to show key off drain. Explain this is what happens when you leave the lights on! Demonstrate use of ten amp current flow through meter. Demonstrate amp probe to measure higher current flow of alternator output. Measure alternator current flow on vehicle in good condition. Allow students to practice the procedures with instructor observation.

Web Resources for Step 5

Title: Alternator test site
URL: http://nttc.columbiabasin.edu/automotive/electric.htm

Annotation: Training site for alternator testing and meter use

Step:  6

Set up several vehicles and /or modules with working electrical systems. Divide students into teams. Have students use attached work sheets to practice for performance test. Observe and monitor student progress. Set up several belt types with access to proper tools for module or vehicle used. Demonstrate proper changing and adjustment of belt.  Facilitate the measurement and comparison of good and defective parts. Set up a few “bugged” components to challenge students. Encourage all students to practice the job skills for the performance test. Allow students to refer to Web sites for review of theory and test procedures.

Step:  7

Allow students to practice and complete work sheets and performance tests. Rubric for assessment is the performance test.

Attachments for Step 7

Title: Work sheet

FileName: Checking a charging system

URL:  http://PDF/ws/charging_WS.pdf
Description: Work sheet is used by student to practice tasks skills in lab.

Title: Work sheet

FileName: Changing a drive belt

URL:  http://PDF/ws/adjdrivebelt_WS.pdf
Description: Work sheet is used by student to practice tasks skills in lab

Title: Work sheet

FileName: Replacing an Alternator

URL:  http://PDF/ws/replacealternator_WS.pdf
Description: Work sheet is used by student to practice tasks skills in lab.

Title: Electrical Theory and Basic Electrical Systems
URL:  https://www.autoteacher.net/Electrical_Performance_TC1I.html

Annotation:

Use the performance tests as needed to have students prove mastery of subject. Performance test may be modified to meet your class/lab and learner needs.

Attachments for Learning Experiences: Please list.

Notes & Reflections:

Students should have unit on basic electrical and battery service and safety completed satisfactorily before beginning this advanced unit. Instructor should insure student follow correct procedures in handling and testing of batteries and electrical components. Review hazards of hydrogen gas and battery acid handling issues. Warn student of dangers of running engine. This unit does not cover Hybrids or High Voltage electric vehicles.

It is assumed that the instructor will instruct students in the dangers of electrical testing on live engines.

It is assumed that:

*	all students will receive instruction in the storage, handling, and use of Hazardous Materials as required in Hazard Communication Title 29, Code of Federal Regulation Part 1910.1200, ‘Right to Know Law’, and state and local requirements;

*	hazardous and toxic materials will be handled, removed and recycled or disposed of according to federal, state, and local regulations.

Culminating Performance Task (Optional)

Culminating Unit Performance Task Title:

Charging System

Culminating Unit Performance Task Description/Directions/Differentiated Instruction:

When students complete job sheet and have practiced the tasks the instructor may use the attached performance test for final assessment and to prove their level of mastery for unit. The performance test may be used by students during practice for peer assessment before instructor sign off. The completed rubric is placed in student portfolio for future reference

Attachments for Culminating Performance Task: https://www.autoteacher.net/Electrical_Performance_TC1I.html

# Name _____________________ Date_________________     Charging System Service

# NATEF Task Area:  VI. ELECTRICAL/ELECTRONIC SYSTEMS task area VI

Objective; Student will be able to:  safely test, diagnose, service, repair and make necessary corrections to electrical circuits using correct procedures, proper tools, and test equipment

Practice only after instructor demonstration! Ask permission first!

Reference: https://www.autoteacher.net/Electronic_Q3HM.html

| Performance Indicators | Student Check | Instructor Check |
| --- | --- | --- |
|  | 1 2 3 4 | 1 2 3 4 |
| Perform charging system output test; determine necessary action. Diagnose charging system for the cause of undercharge, no-charge, and overcharge conditions. Inspect, adjust, or replace generator (alternator) drive belts, pulleys, and tensioners; check pulley and belt alignment. Remove, inspect, and install generator (alternator). Perform charging circuit voltage drop tests; determine necessary action. Use of reference materials Tool use Proper procedure Diagnosis and answers to electrical questions |  |  |  |  |  |  |  |  |

Student Signature ________________________ Student Check Name_________________

Instructor Signature________________________

Comments:

All repairs and service procedures are to be done in SAFE, Proper manner, All SAFETY Rules Apply! Neat, Clean, and you must wear Safety Glasses at all times. Violation of safety rules will cause testing to terminate with result of negative grade for this performance test.

Scoring:

4 Mastery- Student successfully applied knowledge or performance to all tasks independently.

3 Proficient - Student met knowledge or performance tasks without assistance on most tasks.

2 Basic - Student met knowledge or performance tasks with or without assistance on some tasks.

1 Unacceptable - Student unable to meet knowledge or performance criteria and /or required much assistance.

Unit Resources

Web Resources:

http://nttc.columbiabasin.edu/automotive/electric.htm

https://www.autoteacher.net/Electronic_Q3HM.html

http://www.autoshop101.com/

http://www.changingbelt/video/video.html

Attachment(s):

Materials & Equipment:

- Snap-On VAT–40 or OTC Minuteman equivalent recommended

- Multimeters, Fluke 87 or equivalent recommended with extra lead sets

- Several vehicles with batteries, alternators and/or test modules set up

- Several alternators and charging system parts.

- Reference materials such as factory service manuals, electronic service information, or equivalent, and specifications from electrical component suppliers

- Belts, tensioners and modules or vehicles for student practice of belt replacement.

- Provide safety glasses and protective clothing and cleaning supplies

What 21st Century Technology was used in this unit:

Top of Form

|  | Slide Show Software |  | Graphing Software |  | Audio File(s) |
| --- | --- | --- | --- | --- | --- |
|  | Interactive Whiteboard |  | Calculator |  | Graphic Organizer |
|  | Student Response System |  | Desktop Publishing | x | Image File(s) |
|  | Web Design Software |  | Blog |  | Video |
|  | Animation Software |  | Wiki |  | Electronic Game or Puzzle Maker |
|  | Email | x | Website |  |  |

Bottom of Form

# Text boxes

Transportation