PATHWAY:  Transportation Logistical Operations and Support

COURSE:  Foundations of Transportation Logistics

UNIT 1 : Battery Service and Jump Starting

Introduction

Annotation:

Through the use of lecture, multimedia resources, demonstration, group activities, and hands-on lab work the instructor will direct the student to safely and properly start a vehicle with a discharged battery. The student should have previous training in the service of the automotive battery and components. Students will review instruction in diagnosis and service of batteries, connectors, terminals, clamps, sub-systems, and components. Safety and environmental responsibility will be covered in detail. Safe, clean procedures using recommended service tools and equipment will be included in instruction. Recent advances in automotive batteries should be covered as well as trends in batteries. Theory of operation with emphasis on the lead–acid batteries’ dangers should be covered and reinforced. Procedures should include precautions for SRS (air bags), anti-theft devices, and all of the vehicle's computer systems. Separate instruction should cover High Voltage Systems.

Grade(s):

| x | 9th |
| --- | --- |
| x | 10th |
| x | 11th |
| x | 12th |

Time:  	6 (2 Hour periods)

Author:

Sonny Reeves

sreeves.hutchingscc@bibb.k12.ga.us

www.autoteacher.net

Additional Author(s):

Students with Disabilities:

For students with disabilities, the instructor should refer to the student's IEP to be sure that the accommodations specified are being provided. Instructors should also familiarize themselves with the provisions of Behavior Intervention Plans that may be part of a student's IEP. Frequent consultation with a student's special education instructor will be beneficial in providing appropriate differentiation.

Focus Standards

GPS Focus Standards:

ACT-FTL-1: Demonstrates knowledge of safety, OSHA, EPA issues and procedures.

GPS Academic Standards:

SCSh4. Students will use tools and instruments for observing, measuring, and manipulating scientific equipment and materials.

NATEF 2008 Standards:

- VI B 1: Perform battery state-of-charge test; determine necessary action.

- VI B 2: Perform battery capacity test (or conductance test); confirm proper battery capacity for vehicle application; determine necessary action.

- VI B 3: Maintain or restore electronic memory functions.

- VI B 4: Inspect and clean battery, battery cables, connectors, clamps and hold-downs and/or replace battery.

- VI B 5: Perform battery charge.

- VI B 7: Start a vehicle using jumper cables or an auxiliary power supply.

NATEF Academic Standards:

- LA285: The technician can comprehend and apply information in operator's manuals to operate and maintain automotive tools and equipment.

- MA176: The technician interprets symbols to determine compliance with the manufacturer's specifications.

- SC198: The technician can demonstrate an understanding of the correct procedure to measure the electrical parameters of voltage, current, resistance, or power.

Understandings & Goals

Enduring Understandings:

Battery service is a vital part of maintenance to an automobile. Proper battery service can extend the life of a battery for several more years.

Essential Questions:

What are the OSHA, EPA and safety procedures to know so that work can be safe in an automotive shop?

What are the advantages of proper battery service?

What are Health and Safety procedures that should be followed when working with batteries.

Knowledge from this Unit:

- Students will understand that properly serviced lead acid batteries will last for several years.

- Students will understand unsafe procedure could cause severe harm to themselves and others.

Skills from this Unit:

- How to properly service a battery.

- How to jump start a battery.

- Knowledge of the different parts of a battery.

Assessment(s)

Assessment Method Type: Select one or more of the following. Please consider the type(s) of differentiated instruction you will be using in the classroom.

|  | Pre-test |
| --- | --- |
|  | Objective assessment - multiple-choice, true- false, etc. |
|  | __ Quizzes/Tests __ Unit test |
|  | Group project |
|  | Individual project |
| x | Self-assessment - May include practice quizzes, games, simulations, checklists, etc. |
|  | __ Self-check rubrics __ Self-check during writing/planning process __ Journal reflections on concepts, personal experiences and impact on one’s life __ Reflect on evaluations of work from teachers, business partners, and competition judges __ Academic prompts _x_ Practice quizzes/tests |
| x | Subjective assessment/Informal observations |
|  | __ Essay tests _x_ Observe students working with partners __ Observe students role playing |
| x | Peer-assessment |
|  | __ Peer editing & commentary of products/projects/presentations using rubrics _x_ Peer editing and/or critiquing |
|  | Dialogue and Discussion |
|  | __ Student/teacher conferences __ Partner and small group discussions __ Whole group discussions __ Interaction with/feedback from community members/speakers and business partners |
| x | Constructed Responses |
|  | __ Chart good reading/writing/listening/speaking habits _x_ Application of skills to real-life situations/scenarios |
|  | Post-test |

Assessment(s) Title:

Inspecting and testing a battery.

Assessment(s) Description/Directions:

- Download assessment from http://www.cdxetextbook.com/PDF/ac/testbat_AC.pdf

- Have students follow worksheet for practice and teacher assessment of the practice.

Attachments for Assessment(s):

Work Sheet, Testing a Battery Worksheet, Battery Test

Learning Experiences

Instructional planning: Include lessons, activities and other learning experiences in this section with a brief description of the activities to ensure student acquisition of the knowledge and skills addressed in the standards. Complete the sequence of instruction for each lesson/task in the unit.

Sequence of Instruction

1.  Identify the Standards. Standards should be posted in the classroom for each lesson.

2.  Review Essential Questions.

3.  Identify and review the unit vocabulary.

4.  Assessment Activity.

Step: 1

Begin with review of safety in the use of battery test and charging equipment. Describe and demonstrate how to identify positive and negative terminals. Warn students of the dangers associated with typical lead-acid batteries. Explain how hydrogen gas is produced and its dangers. Explain danger of acids from battery. Demonstrate by placing a few drops of acid and corrosive dust on cotton rag and show students the results the next day. Remind them of what it will do to Tommy’s shirt and pants! Refer to previous lesson on shop safety. Use a live 12-volt automotive battery or vehicle system for this demonstration. Demonstrate what occurs when a direct short is put into a circuit in a controlled, safe manner. Use a covered or remote battery for students to experience safety precautions. You may want to use a dummy battery with a set of dry cell 6-volt batteries to prevent explosions of hydrogen gas. Be sure and stress the dangers of working on live circuits, wet cell batteries, and electrical components. Have students watch video and study the web resources online or use an interactive white board/LCD to display for class.

Web Resources for Step 1

Title: Battery Testing

URL: http://www.cdxetextbook.com/electrical/princ/batteryMain/testbat.html

Video URL: http://www.cdxetextbook.com/electrical/princ/batteryMain/testbat_cable.html

Step: 2

Review electrical principles of voltage, ohms and amperage. Have students access electrical course on Gordon Worobec’s Web site, or show on interactive white board with projector for review. Show theory and operation of battery. Discuss operation and design. Have students research Fluke Web site for information on battery tests, digital multimeters, and testing. Have students research jump starting on Web sites. Many good sites are found just by typing in “jump starting a car” in a search engine. For a live video and pictures with good descriptions have students go to Edmund's Web site. Have examples of battery to pass around in the class to empathize key points of design and electrical principles. NOTE: DRY, never used, display batteries can be obtained from battery suppliers. Do not allow students to handle filled lead acid batteries without protection! Ensure that eye and body wash in case of emergency is available.

Web Resources for Step 2

Title: Electrical Theory
URL: http://gworobec.users.50megs.com/eleccirc.html
Annotation: Online electrical course for review of theory. Site can be used for student training or review.

Title: Jump Start Video 
URL: http://www.edmunds.com/ownership/howto/articles/43793/article.html
Annotation: Online practical training for proper jump starting.

Title: Fluke Meter Training
URL: http://www.fluke.com/application_notes/automotive/circuit.asp?AGID=1&SID=103#volt
Annotation: Online training site for review of testing procedures.

Step:  3

Have students view Web sites for battery information. If shop battery charger and test equipment (VAT) has a video, show and then demonstrate key points. Set up vehicle for demonstration of battery charger and testing. Explain Cold Cranking Amp measurement. Stress importance of proper procedure in testing circuits for voltage and amperage. Do not allow students to damage meters! Make sure they are fused. Add fuse to lead if needed. If you are using a wet cell battery, cover with heavy cloth to prevent/contain explosion. Demonstrate use of voltmeter in low and high voltage mode. Demonstrate use of low/high amps. Demonstrate use of capacitance meter to test battery. Allow students to practice use of meter and measurement tools. Allow students to practice set up of charger. Explain temperature effects on battery charging. Reinforce math skills from earlier lessons. Stress safety!   Lab should be well ventilated!

Web Resources for Step 3

Title: Fluke Multimeter Use Training Site
URL: http://www.fluke.com/application_notes/automotive/beatbook.asp?AGID=1&SID=103
Annotation: Good resource for training students to use multimeters.

Step:  4

Demonstrate the use of jumper cables, and “Jump box” auxiliary power supply on a live vehicle that is in good condition. Show students examples of meter use to test battery voltage throughout circuit. Demonstrate proper hook-up of cables and show how to locate engine ground. Discuss problem of finding a good ground on late model vehicles. Discuss service problems and solutions of the different problems technicians may encounter. Demonstrate use of low amp probe on live vehicle to show key off drain. Explain this is what happens when you leave the lights on. Allow students to practice the procedures with instructor observation. Mock ups or live vehicles may be used. Warn students about anti-theft radios and reset of components.

Step:  5

Prepare (locate) a discharged battery for demonstration to students. It is recommended that this be recorded for later review on PowerPoint or other multimedia. Demonstrate proper equipment and tool use. Stress safety! Demonstrate proper removal and replacement of jumper cables. Demonstrate how to safely remove and replace cables to avoid spark! Explain and demonstrate use of memory saver. Allow students to practice use of special battery service tools. Advanced students can create video, slide show or power point for demonstration of correct procedure.

Step:  6

Set up several vehicles and/or modules with working electrical systems. Divide students into teams. Have students use attached job sheet to practice for performance test. Observe and monitor student progress. Facilitate the measurement and comparison of good and defective batteries. Encourage all students to practice the job skills for the performance test. Allow students to refer to Web sites for review and to obtain specifications.

Web Resources for Step 6

Title: Jump Start Safety Site
URL: http://www.edmunds.com/ownership/howto/articles/43793/article.html
Annotation: This site can be used in classroom instruction and as reference for student review.

Step:  7

Set up vehicles and/or modules for the performances. Allow students to practice and complete job sheets and performance tests.

Attachments for Learning Experiences:

Attachments for Step 7

Title: Battery Jump Start Procedure

FileName: https://www.autoteacher.net/Performance_Tests_6XEQ.html
Description: Students may use Job Sheet to practice jump start procedure. Attention to safety is stressed!

Notes & Reflections:

Safety cannot be reinforced enough. Ensure that students wear safety glasses, mechanics gloves, and protective clothing before cleaning and service of acid batteries. Be aware that batteries can/will explode with deadly force! The acid is hazardous, very corrosive and can cause damage to most surfaces including skin and eyes. An OSHA approved safety shower and eye wash should be accessible by all persons engaged in this lesson. Shop safety issues are to be reviewed and stressed in this lesson. The service information for several late model vehicles should be compared for different recommended emergency starting procedures. The use of a battery charger should include instruction on the model you have available. It is recommended that vehicles with anti-theft sound systems not be used for these test/service procedures. Disconnect air bags and/or use vehicles without the systems. For student practice a module should be used.

Culminating Performance Task (Optional)

Culminating Unit Performance Task Title:

Battery Core Skills 1

Culminating Unit Performance Task Description/Directions/Differentiated Instruction:

When students complete job sheet, and/or follow activity guide and have practiced the tasks the instructor may use the attached performance test for final assessment and to prove their level of mastery for unit. The performance test may be used by students during practice for peer assessment before instructor sign off. The completed rubric is placed in student portfolio for future reference. The performance test may be modified to suit individual teacher/student needs.

Attachments for Culminating Performance Task:

Download copy from URL  https://www.autoteacher.net/Performance_Tests_6XEQ.html

Copy of document:

# Name _____________________ Date_________________    Core Skills Battery 1

# NATEF Task Area:  VI. ELECTRICAL/ELECTRONIC SYSTEMS task area VI

Objective; Student will be able to:  safely test, diagnose, service, repair and make necessary corrections to electrical circuits, components using correct procedures, proper tools, and test equipment

Practice only after instructor demonstration! Ask permission first!

Reference: https://www.autoteacher.net/Foundations.html

Student Signature ________________________ Student Check Name_________________

Instructor Signature________________________

All repairs and service procedures are to be done in SAFE, Proper manner, All SAFETY Rules Apply! Neat, 	Clean, and you must wear Safety Glasses at all times. Violation of safety rules will cause testing to terminate 	with result of negative grade for this performance test.

Scoring:

4 Mastery- Student successfully applied knowledge or performance to all tasks independently.

3 Proficient - Student met knowledge or performance tasks without assistance on most tasks.

2 Basic - Student met knowledge or performance tasks with or without assistance on some tasks.

1 Unacceptable - Student unable to meet knowledge or performance criteria and /or required much

| Performance Indicators | Student Check | Instructor Check |
| --- | --- | --- |
|  | Poor Average Excellent | Poor Average Excellent |
| 1. VI B 1: Perform battery state-of-charge test; determine necessary action. 2. VI B 2: Perform battery capacity test (or conductance test); confirm proper battery capacity for vehicle application; determine necessary action. VI B 3: Maintain or restore electronic memory functions. 3. VI B 4: Inspect and clean battery, battery cables, connectors, clamps and hold-downs and/or replace battery. 4. VI B 5: Perform battery charge. 5. VI B 7: Start a vehicle using jumper cables or an auxiliary power supply. Safety rules Use of reference materials Tool use Proper procedure Diagnosis and answers to electrical questions |  |  |  |  |  |  |

Unit Resources

Web Resources:

Web resources are embedded and annotated in sequence steps.

Additional web resources can be found at https://www.autoteacher.net/Foundations.html

Attachment(s):

Materials & Equipment:

- Industry approved battery fast/slow charger

- Industry approved auxiliary power supply

- Jumper cables

- Snap-On VAT–40 or OTC Minuteman equivalent recommended with inductive amp probe

- Digital Multi meters

- Several vehicles with batteries and/or test modules set up

- Memory saver. Advanced students can create their own.

- Basic hand tools and special service tools for vehicles being used

- Battery Capacitance Tester

- Electronic service information and specifications from battery and electrical component 	suppliers

- Handouts from battery distributors

Provide safety glasses and protective clothing and cleaning supplies.

What 21st Century Technology was used in this unit:

Top of Form

| x | Slide Show Software |  | Graphing Software | x | Audio File(s) |
| --- | --- | --- | --- | --- | --- |
|  | Interactive Whiteboard |  | Calculator |  | Graphic Organizer |
|  | Student Response System |  | Desktop Publishing | x | Image File(s) |
|  | Web Design Software |  | Blog | x | Video |
|  | Animation Software |  | Wiki |  | Electronic Game or Puzzle Maker |
|  | Email | x | Website |  |  |

Bottom of Form

# Text boxes

Transportation